## Slide 1: DRONE (COPTER-TYPE) AND ARDUPILOT
Presented By NHân

## Slide 2: I. Drone.
Drone definition and classification.
Copter configuration.
Copter-type drone principle.
Basic structure.
Motor control and ESC.
Sensors/receivers.
Flight controllers and companion computers.

## Slide 3: DRONE DEFINITION AND CLASSIFICATION
Copter-based drone:
Aeroplane-based drone (fixed-wing drone):
Drones are defined as aircrafts without any human pilot, crew, or passengers onboard.

## Slide 4: COPTER CONFIGURATION

## Slide 5: COPTER-TYPE (4 MOTORS) PRINCIPLE

## Slide 6: BASIC STRUCTURE

## Slide 7: MOTOR CONTROL
DC 3-phase brushless motors.
ESCs are used as a medium to control motors from flight controller.
ESC protocol: PWM, Oneshot, DSHOT, Multishot,...

## Slide 8: SENSORS/RECEIVER
Accelerometer & Gyrometers: Measure tilt angle, acceleration (velocity can also be derived from acceleration signal).
Antenna: Receive control signal from users via RC/wifi (telemetry in general).
GPS (optional): Locate global position of the robot (longitude, latitude).
Barometer: Measure (high) altitude of the robot.
Camera: Capture picture and video for instant processing using AI or collecting data.
Compass (optional): Determine drone direction.
IR camera/sensor (optional): Human detection.
LIDAR: Altitude hold and object avoidance.

## Slide 9: FLIGHT CONTROLLER AND COMPANION COMPUTER
Flight controller:
Main processor of the drone.
Read input value from the sensor and return output signal to control motors and servos.
Communicate with ground control station.
Companion computer (microcontrollers with telemetry connection are mainly used):
Execute AI task (optional) using camera image/IR camera/IR sensor input.
Determine trajectory for the drone.

## Slide 10: DRONE CONTROL DIAGRAM

## Slide 12: II. ArduPilot
ArduPilot is a trusted, versatile, and open source autopilot system supporting many vehicle types: multi-copters, traditional helicopters, fixed wing aircraft, boats, submarines, rovers and more.
ArduPilot architecture for copter-type drone.
ArduPilot functionalities.
2.1. Firmware.
2.2. Software.
2.3. Simulation.
2.4. Unmanned vehicles.
2.5. Ground control stations.

## Slide 13: ARDUPILOT ARCHITECTURE FOR COPTER-TYPE DRONE

## Slide 14: ARDUPILOT FUNCTIONALITIES
Firmware: Help to communicate with peripherals and allow developers to calibrate them.
Software: Combined with applications such as Mission Plannar or X Plane, ArduPilot can provide a GUI for control.
Simulation: Virtual hardwares are available for developers to test their code before experimenting on real model.
Unmanned vehicles: Support multiple configuration of copters and other unmanned vehicles.
Ground control stations: Supports piloting process and streaming live video and data to the control center.

## Slide 15: FIRMWARE
ArduPilot provides a variety of libraries supporting multiple widely-used peripherals including:
Accelerometers.
Gyroscopes.
Barometer.
GPS.
Compass.
Motors/servos.
and more...

## Slide 16: SOFTWARE

## Slide 17: SIMULATION

## Slide 18: UNMANNED VEHICLES

## Slide 19: GROUND CONTROL STATION

## Slide 20: III. Real-time Robotics
Hardware.
1.1. Frame manufacturing.
1.2. Self-design boards and battery packaging.
Firmwares.
Software - GUI.
AI.

## Slide 21: FRAME MANUFACTURING
The outer parts of the drone’s body are self-crafted using carbon fiber as the main materials. For experimental models, they are made by alluminium or 3D-printed.

## Slide 22: SELF-DESIGNED BOARDS AND BATTERY PACKAGING
There are various boards and module here are self-designed:
- Extended boards for peripherals connecting to the flight controller.
- Compass module.
- BMS (Battery Management System) module.
Also, battery packs of the drone are also created here (including experimenting and grouping the batteries).

## Slide 23
Firmware
Motors (ESC) and sensors calibration
GPS optimization
Battery management